## Slide 1
Flood Forecasting as a tool for Flood Management
Laura Wignall

## Slide 2
Background
www.wisecdt.org
Urban flooding causes enormous economic and social loss.
The contribution of flood risk to the average annual loss on a global level is estimated at US$104 billion (United Nations, 2015).
Hydroinformatics tools such as flood models are valuable assets for an integrated flood management approach, and ultimately reducing the risks faced in urban areas (Henonin et al., 2013).

## Slide 3
www.wisecdt.org
Flood Forecasting Techniques and Methodologies
Hydrological model - used to simulate surface runoff, used as input for hydrodynamic model
Hydrodynamic models - simulates flow in pipes, streets and storage of water on surface. Characterised by dimensionality. For example:
  1D- pipes in a sewer or surface channel
  2D- surface flow model
  Coupled 1D-1D, or 1D-2D- combination of the above

## Slide 4
www.wisecdt.org
Flood Forecasting Techniques and Methodologies
Real-time flood forecasting methods
Empirical scenarios-based system
  -use a rainfall forecast as an input for empirical scenario selections
  -based on historical events
  -no hydraulic model
  -can be relatively simple, for example based around a rain gauge record with the warning levels based on previous experience
Pre-simulated scenarios-based system
  -rainfall forecast as input
  -selects from pre-determined scenarios which are based on hydraulic simulations
Real-time simulations-based system
  -Uses a real-time flood forecast with online hydraulic models

## Slide 5
Identify flood simulation models suitable for this study. For example, DHI MIKE Suite, CADDIES.
Identify and study details of flood forecasting tools which have been used for flood forecasting at different scales.
Identify potential areas for improvement of the above tools
Familiarize with the previously identified models, by using data from previous studies to run models. For example, PEARL
Explore ongoing related projects and investigate any possible opportunities. Potential projects include: CHANSE, PEARL, GII etc.
www.wisecdt.org
Proposed Methodology

## Slide 6
As an original piece of work, identify an initial case study to use, and carry out the following steps:
  Collect and analyse data
  Calibrate model and validate model, subject to data availability
  Analyse model output
  Identify how model can be improved or be adapted for further uses
  Compare output from different models
Case studies that may be used throughout the project may include: cases from EA 2D models benchmarking report, other UK urban catchment, Mauritius, Gandak/Ganges catchment river system.
Drawing on the findings and results, identify a focus and methodology to further develop and investigate.
www.wisecdt.org
Proposed Methodology

## Slide 7
Thanks for listening. Any questions?
www.wisecdt.org