## Slide 1
A probabilistic modelling approach to assessing the risks to groundwater contamination from hydraulic fracturing for a UK shale gas industry
Olivia Milton-Thompson

## Slide 2
www.wisecdt.org
Conventional abandoned oil well
Unconventional oil well
a
b
a
d
c
e
Shale
Chalk Aquifer
Impermeable Rock
Permeable Rock
b
a
d
c
e
Well integrity failure
Infiltration
Fracture propagation
Natural fracture connection
Connection with old oil well
Contaminant transport pathway

## Slide 3
www.wisecdt.org
Well Integrity
Formation
B
A
E
D
C
PATHWAYS
A Through fractures in the cement
B Between cement and casing
C Through the cement
D Between cement and formation
E Through gaps in the cement
SOURCE
Hydrocarbon reservoir
Permeable formations
Coal seams
Biogenic/thermogenic gases
RECEPTOR
Groundwater
Casing
Cement

## Slide 4
www.wisecdt.org
Code Violations
Highlighted all code violations linked to well integrity from the Pennsylvania database between 2009-2014
Code | Description
78.73A, 78.73B, 78.81D1 | Improper pressure control
78.82, 78.83GRNDWTR, 78.84, 78.86* | Improper casing to protect fresh groundwater
78.81D2, 78.83A, 78.83(c), 78.83COALCSG, 79.12CW | Improper casing and cementing procedures
78.81(a)2, 78.81(a)3, 207B, OGA 3217(B) | Improper casing and cement to prevent migration to fresh groundwater
78.85 | Improper cement installation
78.91(a), 210INADPLUG, 210NCPLUG | Inadequate or leaking plug to prevent vertical flow
3.8% are violations (16,041 wells drilled)

## Slide 5
www.wisecdt.org
Current and Future Work
Improve the data:
A more accurate search is needed to find all violations – needs to include key words from the comments section.
To analyse the data from 2015 to current (violation codes changed).
Create the model:
Develop a simple numerical model to quantify well violations to produce the probability distribution function.
Write the report:
Produce a report/paper on the development of Features, Events and Processes from hydraulic fracturing.